## Slide 1: Code Optimization using Code Re-ordering
Presented by,
Arangamanikkannan Manickam

## Slide 2: Introduction
Code optimization is needed to fully utilize the existing memory and processor.
Code reordering improves the spatial locality of programs without introducing any hardware cost.
Code reordering re-arranges the code in such a way that the processor is not left idle.
Basic block reordering, procedure reordering etc., are some types of reordering
It reduces instruction miss rate, execution time and power consumption

## Slide 3: Overview
Code re-ordering techniques
Exceeded branches in code reordering
Techniques to overcome exceeded branches

## Slide 4: Basic Block-remapping Algorithm
Proposed by McFarling in 1989
Block execution frequency is used for reordering
Finite state machine is used to recognize instruction reference patterns

## Slide 5: PH Algorithm
Proposed for Hewlett-Packard Precision Architecture (PA-RISC) by Pettis and Hansen in 1990
Two prototypes were proposed
  Placed on top of linker  whole procedures
  Placed on top of existing optimizer  basic blocks
“Closest is best” strategy is used
Basic block chains are identified and ordered using branch heuristics.
Edge execution frequency is used as a reordering criterion

## Slide 6: PH Algorithm
Call graph is built by traversing edges in decreasing edge weight order with “closest is best strategy” using
  Basic block reordering
    Done by block execution frequency
  Procedure reordering
    Done by edge execution frequency  undirected weighted call graph is built using the collected profiling data
  Procedure splitting
    Process of separating less executed basic blocks of a procedure in a separate region
    More procedure come under single page
10
4

## Slide 7: Cache line-coloring Algorithm
Proposed by Hashemi in 1997
Reduces cache conflict misses
Call graph, procedure size, cacha line size are considered
Accurately map procedures in a “popular call graph”
It avoids caller-callee conflict
It improves the work oh of PH algorithm
It can be used with different levels of granularity (procedures, basic blocks) and both intra and inter procedurally.

## Slide 8: Cache line-coloring Algorithm
Build program call graph
  nodes represent procedures
  edges represent calls
  edge weight represent call frequencies
Prune edges based on a threshold value
Sort graph edges and process in decreasing edge weight order
Place procedures in the cache space, avoiding color conflicts
Fill in gaps with remaining procedures
Reduces execution time by up to 49% for data compression algorithms

## Slide 9: CMG Algorithm
Propose by Kalamatianos in 1998
Enhanced cache line coloring algorithm by considering higher order conflict misses
He used Conflict Miss Graph (CMG) for procedure level temporal interaction
  Edge weight  it is the approximation of the worst case number of misses between two competing procedures
  Color based mapping is done to reduce conflict misses

## Slide 10: Heuristic approach
Proposed by Parameswaran in 2001
Heuristic approach is taken to relocate code in main memory to reduce conflict misses.
Basic block execution frequency is used for reordering
High frequency blocks are placed next to each other within cache
It works on basic block level
To reduce conflict misses, blocks spread apart in memory and gaps are filled by later blocks, but memory required is increased.
Fetch efficiency is not fully utilized.

## Slide 11: Exceeded Branches in Code-reordering
A
A
B
BB
C
D
A
A
B
BB
C
D
Exceeded?
0
0
1000
1000
0
0
1000
1000
T
F
F
T

## Slide 12: Factors Related with Exceeded Branches
Total number of instructions
Total number of executed instructions
Interleaving of hot and cold code

## Slide 13: Code reordering on Limited Branch Offset
Three methods are proposed
  Direct jumping method
  Distant jumping method
  Bidirectional code layout algorithm

## Slide 14: Direct Jumping Method
A
Jump fall-through
Jump remote target
C
D
B
Fall through
Remote target
Two unconditional jumps are introduced
In MIPS, 26-bit offset
Continuous control flow instructions are not preferred.
It pollutes the cache

## Slide 15: Distant Jumping Method
Only a single jump is inserted
Hottest part of the code is packed together
Cold density is also high  reduced cache miss rate.
A
C
D
X
Jump remote- target
Y
B
Fall through
Remote target
No relations

## Slide 16: Bidirectional Code Layout Algorithm
Hot code is kept in the center and less frequent code are placed both forward and backward.
Distance between hot and cold code are reduced.

## Slide 17: Bidirectional Code Layout Algorithm Steps
Basic block chaining
  Edges are sorted in descending order and connect basic blocks with highest count
Super chain forming
  Separate chain in the same function are connected together to improve spatial locality
  The cold chains are also connected together to reduce the occurrence of exceeded branches
Chain layout
  Sort the chain
  Select hottest chain and lay it next to the prior chain selected

## Slide 18: Conclusion
Various code reordering techniques and their advantages and disadvantages are studied.
Methods to overcome exceeded branches in code ordering are also studied.

## Slide 19: References
MCFARLING, S. 1989. Program optimization for instruction caches. In Proceedings of the 3rd International Conference on Architectural Support for Programming Languages and Operating Systems, Boston, MA (Apr.). 183–191.
PETTIS, K. AND HANSEN, R. 1990. Profile guided code positioning. In Proceedings of the ACM SIGPLAN Conference on Programming Language Design and Implementation, White Plains, NY (Jun.). 16–27.
HASHEMI, A. H., KAELI, D. R., AND CALDER, B. 1997. Efficient procedure mapping using cache line coloring. In Proceedings of the ACM SIGPLAN 1997 Conference on Programming Language Design and Implementation, Las Vegas, Nevada (June). 171–182.
PARAMESWARAN, S. AND HENKEL, J. 2001. I-CoPES: Fast instruction code placement for embedded systems to improve performance and energy efficiency. In Proceedings of International Conference on Computer Aided Design, San Jose, CA (Nov.). 635–641.
PARAMESWARAN, S. AND HENKEL, J. 2004. REMcode: Relocating embedded code for improving system efficiency. IEE Proc.-Comput. Digit. Tech. 151, 11 (Nov.), 431–435.